## Slide 1: Evaluating LargeBoom & SmallBoom RISC-V CPU performance with EEMBC CoreMark
Presented by - Lalit Prasad Peri (lalitprasad@vt.edu)
Project Group #2
ECE5504 Computer Architecture - Fall2023

## Slide 2: Outline of Presentation
Motivation
Evaluation Methods used
  Static Analysis (ISA / Compiler / Code-Analysis)
  Dynamic Analysis (Runtime / Model Simulations)
Preliminary Results & Takeaway

## Slide 3: Motivation
Synthetic microbenchmarks like Dhrystone (DMIPS) have long been leveraged by CPU architects to fine-tune microarchitecture performance but it is shown to be susceptible to “gaming” by compiler.
Often, if not always, synthetic benchmark scores don’t translate to actionable performance uplifts when comparing CPU architectures (DMIPS, BogoMIPS)
What is CoreMark? CoreMark is a simple, yet sophisticated benchmark that is designed specifically to test the functionality of a processor core. Running CoreMark produces a single-number score allowing users to make quick comparisons between processors.
CoreMark, though having a small program footprint, has a set of diverse algorithms to evaluate performance – i) List processing (search and sort), ii) matrix manipulation, iii) finite state machine, and iv) CRC (cyclic redundancy checks). Benchmark was designed with 64-bit processors in view.
How Coremark Improves on Dhrystone? Like Dhrystone, CoreMark is small, portable, easy to understand, free, and displays a single number benchmark score. Unlike Dhrystone, CoreMark has specific run and reporting rules, and was designed to avoid problematic aspects of Dhrystone (i.e. library optimizations)
As the outcome of this study, intention is to recommend a high-performance CPU microarchitecture for either class of RISC-V designs i.e., LargeBoom & SmallBoom, optimized for workloads which have similar characteristics as CoreMark.

## Slide 4: Evaluation Method
Static Analysis (ISA / Compiler / Code-Analysis)
Focuses on static analysis & optimization of binaries by the means of using compiler and profile-guided optimizations.
In this step extract the characteristics like code-footprint, instruction mix and function graph profiles (CFGs).
Since benchmarks could be “gamed” to improve scores without tangible changes in CPU architecture, this necessitates to understand the possible signatures of static optimizations.
For this gnu-gcc-9.4.0 is used for x86 and RISC-V extension riscv64-unknown-elf-gcc for SmallBoom / LargeBoom.
Some of the flags explored - -O1, -O2, -O3, -Ofast, -funroll_loops, -ftree_vectorize

## Slide 5: Evaluation Method
Dynamic Analysis (Runtime / Model Simulations)
Dynamic analysis focuses on simulating and observing the sensitivity of benchmarks with micro-architecture parameter variations. This study proposes to use chip-yard project which instantiates scala-models for CPUs and supports LLC and main memory, with parameterizable characteristics.
Micro-architecture features | Policies and parameter sweeps
Caches | Replacement policies – LRU, SLRU, Random $Sweeps - Line-sizes, sets/ways
Prefetchers | NLP, NLP+N, SWPrefetch
TLB | iTLB/dTLB sizes. PageTable Entries.
Branch-prediction | PHT/BTB sizes; SwPred, TAGE, Alpha
Instruction-Scheduling | INT/FP phy-registers, ROB size, Ldq/Stq

## Slide 6: Preliminary Results #1
Static Analysis (ISA / Compiler / Code-Analysis)
By generating objdump / de-compilation of coremark binaries, instruction mix was extracted.
Ghidra Decompiler also used to extract object decompliation.
Hurdles overcome: CPU_CYCLE macros in source codes as gcc risc-v doesn’t have complete/correct implementation of <time.h>. Instrumenting coremark source code for RISC-V performance counters.
Chart: CoreMark/MHz
| "-O0" | "-O1" | "-O2" | "-O3" | "-Ofast" | "-funroll_loop"
CoreMarks/MHz | 2.0464 | 6.6355 | 8.9085 | 8.7657 | 8.7693 | 9.1586
IPC | 0.56 | 0.63 | 0.74 | 0.63 | 0.5 | 0.66
Ghidra-decompiler
Chart: Instructions / Branch_Density
| "-O0" | "-O1" | "-O2" | "-O3" | "-Ofast" | "-funroll"
Instruction (million) | 136531.1465 | 143901.0416 | 356106.9758 | 278958.4098 | 305538.4231 | 362658.8279
Branches(%) | 0.199 | 0.199 | 0.199 | 0.199 | 0.199 | 0.199

## Slide 7: Preliminary Results #2
Dynamic Analysis ( Runtime / Model Simulations)
Preliminary profiling results on x86 server (for comparison with RISC-V model profiling).
Chart: Instruction - retiring / Stalls
| "-O0" | "-O1" | "-O2" | "-O3" | "-Ofast" | "-funroll_loop"
Stalls_FE | 15.03 | 15.04 | 15.02 | 15.01 | 15.02 | 15.01
Stalls_BE | 25.02 | 24.97 | 24.99 | 24.97 | 24.99 | 25
Br_Mispred | 19.9 | 19.9 | 19.9 | 19.9 | 19.9 | 19.9
Retiring | 40.05 | 40.09 | 40.09 | 40.12 | 40.09 | 40.09
Chart: Misses Per Kilo Instruction
| "-O0" | "-O1" | "-O2" | "-O3" | "-Ofast" | "-funroll_loop"
L1d_MPKI | 5.8266 | 6.8059 | 5.1839 | 5.4978 | 8.1381 | 9.5683
L1i_MPKI | 10.0142 | 9.1221 | 7.9441 | 9.4273 | 7.2572 | 8.1948
dTLB_MPKI | 0.32157 | 0.26024 | 0.27033 | 0.3233 | 0.42225 | 0.3809
iTLB_MPKI | 0.058196 | 0.038242 | 0.043938 | 0.050474 | 0.090884 | 0.069753
Br_Mispred_PKI | 4.8397 | 5.3199 | 3.5734 | 5.1383 | 5.3372 | 5.4357
Higher L1i/L1d miss rates!

## Slide 8: References [1] Shay Gal-On, Markus Levy, “Exploring CoreMark™ – A Benchmark Maximizing Simplicity and Efficacy” EEMBC Whitepaper [2] Jim Turley “Dhrystone Is Dead; Long Live CoreMark!”, EEJournel, June’2009 [3] CoreMark-Cortex-M4. https://developer.arm.com/Processors/Cortex-M4 [4] SimulationArtifacts: https://github.com/lalitprasadperi/Evaluating_CoreMark_on_BoomCore [5] RISC-V Insstruction Set Architecture v2.2 https://riscv.org/wpcontent/uploads/2017/05/riscv-spec-v2.2.pdf [6] BOOM CPU Specification https://docs.boom-core.org/en/latest/ [7] Chipyard Project Documentation https://chipyard.readthedocs.io/en/latest/Generators/BOOM.html [8] Gcc-riscv toolchain https://wiki.riscv.org/display/HOME/Toolchain+Projects [9] David A Patterson and John L. Hennessy, Computer Architecture: A Quantitative Approach 5th edition. [10] Course Slides, ECE5504 Fall2023

## Slide 9: Q & A